## Slide 1: Bus and Coach PBS Issues
Luke Hardy Bus Industry Confederation

## Slide 2: Bus and Coach Industry
The Australian Bus Industry in Brief:
As of January 2011, there were 87,883 registered buses in Australia.(1)
These buses are operated by more than 3,000 bus companies across the country.(2)
More than 50,000 people are employed in the Australian bus industry with 10,000 people working in the bus manufacturing sector. (2)
The bus industry services 1.5 billion urban public transport passengers per year.
The coach sector of the industry move more than 1.6 million domestic travellers per year. (3)
Typically there are around 1500 new buses delivered to the Australian market annually. (4)

## Slide 3: BUS and Coach PBS
PBS in the Bus and Coach Industry
The ADR’s allow for rigid buses up to 12.5 m in length and articulated buses up to 18 m in length.
PBS is used for higher capacity buses which do not fall into the traditional ADR bus sizes.
Buses that have been through the PBS process include some of the high passenger capacity 14.5 m rigid city buses and three axle 13.5 m coaches.
High passenger capacity buses, super buses, (longer vehicles , bi-tri articulated and double deckers) are not being introduced due partly to restricted road access.
Such restrictions are due to a range of issues not just PBS.

## Slide 4: PBS Bus and Coach Numbers
Uptake of PBS in the bus industry is quite low.
The graph shows that up until 2011 only 4% of the total PBS applications processed were for buses or coaches(5) and this trend has not changed in recent times.
This figure is low considering the productivity improvements of higher capacity buses and coaches which , depending on type and configuration, can increase passenger capacity from 15% up to 50%.

## Slide 5: Why the Low PBS Numbers?
In summary, the reasons are:
Various States allow for 14.5 m buses without needing PBS (NSW, ACT, QLD, etc.). Hence operators take this option.
Buses typically perform very well in all of PBS aspects except the areas of:
  Low Speed Swept Path
  Frontal Swing
  and Tail Swing.
Some of the reasons for this are:
  The need to comply with the DDA (front door width to accommodate Wheelchair Ramps, hence long front overhangs),
  Variations in Rear Overhang from State to State, QLD 4.7 metres or 70% wheelbase, NSW 4.9 metres or 70% wheelbase, VIC - 4.3 m or 60% wheelbase.

## Slide 6: Why the Low PBS Numbers?
  Low Level of PBS take-up continued:
  The steerable tag 13.5 and 14.5 m buses are especially effected by tail swing, but these buses perform very well on the road.
The general level of knowledge of PBS in the Bus and Coach industry is low.
There needs to be Bus and Coach specific modelling developed and agreed.
PBS needs to be futher promoted within the Bus and Coach Industry by BIC.
In the end, the Bus and Coach Industry needs to be more actively involved with NHVR and the NTC.

## Slide 7: Bus and Coach Industry
END OF PRESENTATION
References:
(1) ABS Census of motor vehicle – January 2011.
(2) 2010, Industry Survey, Bus Industry Confederation of Australia, Canberra
(3) Tourism Research Australia, 2008, Transport Fact Sheet, Department of Resources, Energy and Tourism, Canberra.
(4) Bus Industry Confederation, 2011, Based on bus sales data recorded in Australasian Bus and Coach Magazine.
(5) National Transport Commission Performance Based Standards – Regulatory Impact Statement December 2011 ISBN: 978-1-921604-8.