## Slide 1: Approving sub-assemblies and key components
by Peter Heatley - Michelin

## Slide 2: Approving sub-assemblies and key components
The tyre is the only point in contact with the road
Apart from carrying the load it provides the means for steering braking & cornering
Notes: Not an expert on tyre modelling.
6 degrees of freedom model
<number>

## Slide 3: Approving sub-assemblies and key components
PBS submissions require the use of tyre data assessors to establish vehicle performance
Data required is self aligning moment & cornering force
These measurements are not automatically conducted on all tyres
Original equipment manufacturers use longitudinal & lateral stiffness in vehicle design
Notes: A tyre when rolling freely in a direction when subject to side force ( camber / wind) will follow a path at an angle to the original direction. The difference between vehicle & tyre is Slip angle Lateral force requires a slip angle. Slip angle means there is lateral force.
Self aligning force is the resistance of the tyre to distort in the contact patch.
<number>

## Slide 4: Approving sub-assemblies and key components
Self Aligning Torque
Cornering Force

## Slide 5: Approving sub-assemblies and key components
Measurements conducted in approved laboratories
Process subject to audit
Notes: Testing facilities are subject to audit for compliance
<number>

## Slide 6: Approving sub-assemblies and key components
Longitudinal Stiffness
Lateral Stiffness
Notes: Trailer tyres are not measured in particular
Vehicle manufacturers have played a role in these models to improve safety
Small market with low volume traditional dimensions
<number>

## Slide 7: Approving sub-assemblies and key components
Three categories of truck tyres – Front axle, Drive axle, trailer axle
All have differing design requirements – Steering input , torque applied, load carrying
Notes: The influence of tyre stiffness is related to load/pressure rim width. Road surface/ weather conditions & vehicle speed also contribute
<number>

## Slide 8: Approving sub-assemblies and key components
All data should be held by central administration to validate authenticity - NHVR
Potential to grade products – A, B, C etc.
End users contacting requesting PBS approved tyres
Roadside service issues
Can a PBS vehicle use re-treads?
Notes: Holding of data by central point to ensure real data is available.
Grading of products to protect intellectual property
Consider the operators requirement to purchase tyres
Consider some replacement of tyres occurs in the field
For reduced tyre costs can we use retread for PBS vehicles? Different casing with different age & different tread compound
<number>

## Slide 9: Thank you