## Slide 2: Review of Performance Based Standards for Level 3 and 4 vehicles
Marcus Coleman
PBS Conference – 6 March 2013

## Slide 3: Context
Limited uptake of Level 3 and 4 vehicles
Alternative schemes facilitating safer and more productive vehicles
Desire for a nationally consistent framework
Notes: Limited uptake of Level 3 and 4 vehicles because PBS offers little advantage compared with vehicles available under alternative schemes
Non PBS combinations have provided safety and productivity benefits and yet are unable to meet PBS requirements

## Slide 4: Key Questions
What is limiting the uptake of Level 3 and 4 vehicles?
How can the standards be changed to encourage safer and more productive Level 3 and 4 vehicles?

## Slide 5: Key Questions
How do we currently define safer and more productive?
Can we redefine safer?

## Slide 6: Key Questions
Which standards are limiting the uptake of Level 3 and 4 vehicles?
  Infrastructure
  Powertrain
  Length and Width
  Low Speed Turning
  High Speed Stability

## Slide 7: Infrastructure Standards
Pavement horizontal loading
Bridge

## Slide 8: Powertrain
Performance Standard | Level 3 | Level 4
Startability | At least 10% | At least 5%
Gradeability (A) | At least 12% | At least 8%
Gradeability (B) | At least 70km/h | At least 60km/h
Acceleration Capability | 26 seconds | 29 seconds

## Slide 9: Length

## Slide 10: Width

## Slide 11: Low Speed Turning
Performance Standard | Level 3 | Level 4
Low Speed Swepth Path | 10.6m | 13.7m
Frontal Swing | 0.7m | 0.7m
MOD | 0.4m | 0.4m
DOM | 0.2m | 0.2m
Tail Swing | 0.35m | 0.50m
STFD | 80% | 80%

## Slide 12: High Speed Stability
Performance Standard | Level 3 | Level 4
Static Rollover Threshold | 0.35g / 0.4g | 0.35g / 0.4g
Rearward Amplification | 5.7xSRT | 5.7xSRT
High Speed Transient Offtracking | 1.0m | 1.2m
Yaw Damping Coefficient | 0.15 | 0.15
Directional Stability Under Braking | 0.25g | 0.20g

## Slide 13: Milestones
Stage 1: Discussion Paper (Apr ‘13)
Stage 2: Validation of assessment methods (May ‘13)
Stage 3: PBS Assessment of existing fleet (Sep ‘13)
Stage 4: Draft Report (Nov ‘13)
Stage 5: Final Report (Jan ‘14)

## Slide 14: End