## Slide 1: Airbag Suspension Parameters for PBS
Mario Colosimo

## Slide 2: Airbag Suspension Parameters for PBS
1. Roll Stiffness
2. Roll Steer
3. Roll Centre Height

## Slide 3: Roll Stiffness
With trailing arm type airbag suspensions, there are two elements to the roll stiffness;
Roll Stiffness due to the airbags
Auxiliary roll stiffness

## Slide 4: Roll Stiffness due to the Airbags
Roll Angle
With throttled crossflow the airbags contribute approx. 15% of roll stiffness

## Slide 5: Auxiliary Roll Stiffness
Pivot
Rigid attachment
When the axle rolls about the roll centre, the trailing arm spring bends and the axle beam twists

## Slide 6: Roll Centre Height
The Roll Centre of the suspension is along the centre of the vehicle, at the height of the suspension pivots

## Slide 7: Roll Centre Height
430mm
5°Roll Angle
430mm
720mm
158mm
184mm
2540mm
Example, approx 15% difference in lateral shift of CoG due to different Roll Centre Height – without suspension and tyre deflection

## Slide 8: Roll Steer
The axle moves in an arc around the front pivots. It does not just move up and down, it moves backwards and forwards at the same time.
When the axle rolls about the roll centre, or tilts, one wheel moves up and the other down, so one wheel will move forward and the other backwards, effectively steering.

## Slide 9: Roll Steer
Roll Steer depends on the length of the trailing arm, and the difference in height between the axle centre and the pivot point.
Underslung suspensions will generally steer into corners, overslung suspension will steer out of a corner.
The Roll Steer coefficient is a measure of the amount of steer relative to the roll on the suspension.
Underslung Suspension
Overslung Suspension

## Slide 10: Airbag Suspension Parameters for PBS
Roll Stiffness
To improve, throttle crossflow between the airbags.
Roll Steer
Underslung suspensions better, and overslung suspensions with the axle height close to the pivot height
Roll Centre Height
Overslung suspensions better, suspensions with a larger distance between the axle and the pivot height will have a higher roll centre